## Slide 1: The University of Chicago PSEC Group Goals, Status, and Requests
Andrey Elagin, Henry Frisch, Carla Grosso-Pilcher, Mary Heintz, Rich Northrop,
Eric Oberla, Matt Wetstein; Brooke Adams, SiYang Ling , Eric Spieglan (undergrads)
Enrico Fermi Institute and Physics Department
University of Chicago

## Slide 2: The Large-Area MCP-PMT A Transformational Technology
No competition in time resolution, gain-bandwidth, number of pixels per area, noise
No competition in scalability to large areas
Intrinsically simple and components are cheap
Millions (almost a billion) of pixels per m2 each with psec time resolution opens up opportunities that have never been considered.
WE HAVE FOUND NO SHOW-STOPPERS AND THERE IS NO COMPETITION IN PERFORMANCE
However it is not easy…we have both successes & challenges

## Slide 3: Part I. The Optical Time Projection Chamber
Ph.D Thesis of Eric Oberla- July 31. (to be a NIM paper)
Demonstration device for a new kind of detector- reconstructing tracks using precise measurements of light transit times and arrival locations. Related to possible uses in HEP, nuclear, and security – intended to demonstrate that one can reconstruct tracks in a simple small water volume.
The OTPC installed in the LArIAT beamline in Mcenter at Fermilab
(great name – thanks to Howard Nicholson, who also suggested applying LAPPDs to neutrino detectors)

## Slide 4: The First Optical Time Projection Chamber
Ph.D Thesis of Eric Oberla- July 31. NIM paper
Ports for Planacon MCP-PMTs(3 normal, 2 stereo)
equal spacing in z
Mirror for each Planacon (5)
Muons from LArIAT Beam
Direct Cherenkov Light (prompt)
ReflectedCherenkov Light (1000 psec later)
Water
radiator
11”
30”
Ack. Home Depot

## Slide 5: The OTPC exploits 3 ideas possible only with fast (“psec”) photodetectors
‘Drift’ photons by measuring the arrival times. Measures the distance to photon origin (3D point vs the 2D arrival position)
Multiply effective photocathode area x QE by using mirrors. The prototype design conservatively gains a factor of 2. Exploits the ‘room’ in the time dimension.
Use 50-Ohm transmission-line readout with only half the number of electronics channels by using the ‘bounce’ of unterminated delay lines on the anode (EO)

## Slide 6: `Drifting’ Photons- exploit Cherenkov rad.
The principle of reconstructing the track position and direction is the same in HEP neutrino physics (ANNIE), nuclear neutrino-less double-beta decay (JINST paper), and TOF-PET imaging (prov. patent).
TOF-PET
ANNIE
Double-beta decay

## Slide 7: Longitudinal vs Transverse Phase Space
Each photodetector, in both normal and stereo views, in the OTPC prototype has a corresponding flat mirror that reflects the light going diametrically opposite back onto the detector. Photons can arrive at the same point but are distinguishable by the difference in arrival times. This extra ‘room’ in phase space:
Economically doubles the effective photocathode area (mirrors are much cheaper than tubes);
Measures points on the track via the difference in the arrival times of direct and reflected photons (one gets earlier and the other later for transverse displacements)
May allow some clever designs for large detectors by exploiting the presence of both longitudinal (time) and transverse (position at the photocathodes) phase space to increase coverage more than just twice, and to cover less simple geometries (emittance manipulations like those in accelerators).

## Slide 8: Exploiting the GHz Transmission Line Anode
Eric Oberla
1 end of 50 Ohm TL is unterminated stub
This end read out by PSEC4 ASICS
which see the pulses from both ends of the TL on the same channel- do the autocorrelation read out by PSEC4 ASICS
unterminated stub
PSEC4 ASICS
1024 Planacon pads to 30 TLs

## Slide 9: We see tracks in the water. `Typical Events’
Eric Oberla
Z position along OTPC
Time
Time
Time
Time
Through
Through
Big splat (?)
Showering?
Front-back Trigger
Front-back Trigger
Front-only Trigger
Front-only Trigger
N1
N3
N2
S1
S2
Front
Back
Note: this is pedestal-subtracted raw data . Scale is 0 to -3000 counts

## Slide 10: Preliminary Analysis –Tracks
4”
Eric Oberla
Front
Back
1 nsec

## Slide 11: Resolving the Direct and Reflected Photons
Eric Oberla
1 nsec
Normal
Stereo

## Slide 12: Preliminary Conclusions
These data were taken May 19- Eric has written the analysis programs between then and now, so all is preliminary
The hit-finding efficiency is >=75% of predicted- a victory. The loss is consistent with the deficiency seen in the direct view, consistent with light cut off by the baffle of the MCP-PMT housing (i.e. fixable).
It looks nice. The Demountable LAPPDTM data have ~10X the gain of these Planacons, and should work at least as well over 16X the area/photodetector.
Eric has done a remarkable job- he built the detector basically single-handedly. Detector development makes for good students!* Ph.D thesis and NIM paper next.
*(Steinberger’s question at CERN-
Why do Americans build such lousy detectors and have such good students?)

## Slide 13: Part II. UC Electronics and Readout Systems
PSEC-4 ASIC
30-Channel ACDC Card (5 PSEC-4)
Central Card (4-ACDC;120ch)
180-channel OTPC system

## Slide 14
PSEC4 evaluation board
6-channel, 1.5 GHz, 10-15 GSa/s evaluation module
USB 2.0 / powered over USB
For best results, put in an RF box
Motherboard designed by M. Bodgan (EFI/eshop)
Eric slide (mostly)

## Slide 15
PSEC4 evaluation board
U. Vermont :: ground penetrating radar studies for ‘real-time’ civil infrastructure analysis
Sandia Nat’l Lab: high density readout for fast x-ray diodes
Recent additions: Iowa State, LLNL, … (5 new bds by Sandia)
Map by Eric O.

## Slide 16: Ground penetrating radar: Development of a High Speed UWB GPR for Rebar Detection Advantages in cost, size, power, scalability
Rebar
Copper pipe
Example of PSEC4 Adoption for Road and Bridge Infrastructure: D. Huston’s GPR group at Vermont
Tests using metal bar as a reflection target using the WFS-ASIC system. The goal is to be able to measure reflections from subsurface objects, such as steel reinforcing in concrete and buried utilities.
Operate at road speeds (60 mph)
Capture and process real-time data
Multi-channel
  Physical coverage across width of roadway
Meet or exceed FCC mask requirements
  FCC 02-48 compliant
Compact, modular design
E. Oberla slide (mostly)

## Slide 17: Multichannel systems
60-channel Demountable at the APS Laser Lab
( ANL X-ray Science Division)- dismantled
180-channel self-triggered OTPC at Fermilab
Current Central Card supports 240 channels
Central Cards can be `daisy-chained’ for 480 …

## Slide 18: Working on Gen-II Central Card
Higher-speed and more options for readout:- USB, Ethernet, & 6Gbps/fiber QSFP+;
Can handle 8 ACDC cards for a total of 240 channels per module (twice 1st Gen)- multiple modules can be daisy-chained;
Expanded system, trigger, signal interfaces for flexibility in use:
  one RJ45 connector with LVDS for system integration;
  8 RJ45 connectors with LVDS for Front End Cards (FE)communication.
  SMA inputs to FPGA I/O on front-panel for trigger or optional clock input
  several other SMA inputs on board for app-specific signals
  inputs/outputs from FPGA
Implemented in a widely-used standard: VME32/64X
Design by Mircea Bogdan on Watchman funds: reuses blocks from Wah’s JPARC and other working boards by Mircea

## Slide 19: Gen-II Central Card (Mircea Bogdan)
A 500 MHz sampling VME board by Mircea for KOTO - many of the blocks/components will be re-used in the Gen-II Central Card

## Slide 20: New PSEC-4 MOSIS Run
Although PSEC-4 has short-comings, it works well, is well-documented (long NIM paper), and can sample up to 15 GS/sec with a bandwidth of 1.6 GHz;
ASICs are not easy- decided to double-down on the investment in PSEC-4’s speed and bandwidth;
Sandia (NM) paid the NRE and bought a 2nd run from MOSIS- we piggy-backed and bought 2 lots of 40 chips for 10K$ each (standard price);
MOSIS offered us a deal of 3K$/batch (reduced from 10K) after the NRE if we bought 135K$ total; Iowa, MIT, Sandia-NM, Sandia-CA, and UC have jointly ordered it (1200 chips);
ANNIE, Nu-DOT, Sandia use in short-term--other trials of psec -(<5) resolution wave-form sampling in progress

## Slide 21: Beyond PSEC-4
Main limitation of PSEC-4 is the 256-cell buffer- Eric has gotten the self-triggering to work, so that a global trigger can come in after the signals, but it incurs deadtime and isn’t applicable to high occupancy or high rate applications
We and Gary’s group have been working on PSEC-5, a joining of the PSEC-4 sampling design with Gary’s deep buffer design, but moved from IBM to TSMC. We’ve done much of the front-end, but had to stop as the 2014 ARL funding for this task was cut.
Gary and Innosys (SLC) and us have an SBIR for PSEC-5 development- Hawaii playing the leading role;
Eric has proposed a PSEC-4A that makes minimal changes (sic) to PSEC-4 beyond adding multiple buffering of hits so that it’s deadtimeless for typical neutrino experiments (e.g. ANNIE). Attractive to me (in parallel to PSEC-5) .
(See Kurtis’s talk on the Hawaii/UC coordinated effort )

## Slide 22: Part III. Advanced Designs and Fabrication
IMO all the performance parameters and single steps have been proven (and published) by the collaboration; the main problems we face are related to manufacturability.

## Slide 23: Rationale for Gen-II
For LAPPDTMs to be useful to the HEP, Nuclear, and security communities they have to be affordable- IMO at or less than a Planacon. All the cost at present is in the fabrication- the packaging components are cheap. Need to look ahead to competition.

## Slide 24: Toward an Affordable Gen-II Design
Flat Top Seal
High QE Photocathode
(patent with BNL, RMD)
Performance:
HV and signal
(NIM-A,RSI papers, patent)
High-BW ceramic pkg
Psec Electronics system
(NIM-A paper)
Gen-I LAPPDTM

## Slide 25: Flat Indium Solder Seal
Sealed LAPPDTM
Andrey Elagin, Eric Spieglan, Matt Wetstein
No machining of glass groove
No bulk flow if not level over 8”
No manipulation of window
Easiest with PMT-like cathode fabrication (‘in situ’)
We do not completely understand the metallurgy yet
Sidewall seal seen through window
HOWEVER

## Slide 26: Advanced Photocathode R&D
I. With RMD and BNL (SBIR) we have synthesized the stoichiometric compound K2Cs Sb.
II. PMT-process production of photocathodes (with Luca Cultrera, Ivan Bazarov, Cornell)
  Exposure of predeposited Sb layer to Cs-K2 vapor makes a good K2CsSb cathode (Singer, Sinclair)
  Cultrera has shown that air-exposed Sb produces a competitive Cs3Sb photocathode.
Powder diffraction Xray taken with new UC Bruker- 15nm nanocrystals of >99% pure K2CsSb. Currently learning to sputter it. New kind of bulk material- semiconductor.
Credit: Luca Cultrera

## Slide 27: Monolithic Capacitively-Coupled Ceramic LAPPDTM
Quote Unit Price (100) NRE
Company A $314 $2150
Company B $218 $700
UC Gen-I design uses internal HV divider with HV applied through metalized window border and anode strips that extend through the bottom frit seal for DC gd and signal outputs - no external pins
We are exploring a Gen-II ceramic design that allows pads for high-occupancy applications to solve the ‘disambiguation’ problem and that should have X3 the bandwidth, and requires no fritting. (Ceramic is also much stronger than glass) Could be used with Incom mini-SSL transfer process. In the middle of specifying for quotes- present status:
Green-trimmed full-fire monolithic ceramic LAPPDTM tile base assembly
Resistive or thin Conductive inner ground layer
2D array of pads for readout on bottom (outside) layer

## Slide 28: ‘Ultralight’ R&D Fabrication Facility
Outer vacuum for seal process
Precision load and positioning fixture for seal
Sealed tile (no getter this shot)
RGA on outer vacuum (for now)
Inner vacuum to tile and for bi-alkali vapor
Standard 16.5” ConFlat flange
Tile fixture heated (350C) by quartz lamps underneath
Raspberry Pi process data logger- temperatures (10), pressures, RGA,…
Radical and risky, but scaleable, fast thermal cycle, and based on commercial PMT production process (Burle)
NAIP:Arrows are messed up- don’t believe them.

## Slide 29: UC Needs post-2015-ARL SOW &Budget
There have been two rapid technical developments since we submitted the 2015 SOW and Budget to ARL:
  Eric has proposed PSEC-4A (deadtimeless) as an intermediate step to PSEC-5 , and available sooner;
  With ceramics vendors we are developing a design the green-trim ceramic tile base assembly and it’s surprisingly economical, higher performance, and seems viable.
We would like to ask in the near future for additional funds to do the exploratory work for each of these. We are in the middle of getting bids on the latter and Eric is deep in writing his thesis—at this point can only estimate the budgets:
Estimated Requests
PSEC-4A: 3 mo. Elec. Eng. 48K$
Ceramic LAPPDTM TBA’s: 4 iterations 24K$

## Slide 30: Brief Summary
The water-based Optical Time Projection Chamber concept works nicely and the results agree with Monte-Carlo-based expectations;
PSEC-4 has been adopted by several groups and a number of others have Eval Cards; Iowa/MIT/Sandia-NM/Sandia-CA/UC have ordered 1200 more chips.
We are progressing making the glass LAPPDTMs in the Ultralight scalable tile facility . We can consistently make flat hot seals for the LAPPDTM tiles; working with Indium Corp on intermetallic issues (confidential).
Cornell has promising results on the photocathode process needed for the Ultralight facility ; separately with RMD and BNL we have synthesized the stoichimetric compounds and sputtered alkali cathodes;
We are still in early stages of developing the Gen-II ceramic Tile Base Assembly, but it looks very attractive.

## Slide 31: MCP Timing Performance : B.W. Adams, A. Elagin, H. Frisch, R. Obaid,E. Oberla, A. Vostrikov, R. Wagner, J. Wang, M. Wetstein; Timing Characteristics of Large Area Picosecond Photodetectors Nucl. Inst. Meth. Phys. Res. A. , Vol. 795, pp 1-11 (tbp Sept. 2015); pub.online June 5, 2015.
Fast Timing in Searches for Double Beta Decay C. Aberle, A. Elagin, H.J. Frisch, M. Wetstein, L. Winslow. Measuring Directionality in Double-Beta Decay and Neutrino Interactions with Kiloton-Scale Scintillation Detectors; JINST 9 P06012 doi:10.1088/1748-0221/9/06/ (June 2014) P06012arXiv:1307.5813
No-pin Internal HV Circuit B. W. Adams, A. Elagin, J. W. Elam, H. J. Frisch, J.-F. Genat,J. S. Gregar, A. U. Mane, M. J. Minot, R. Northrop, R. Obaid,E. Oberla, A. Vostrikov, M. Wetstein; An Internal ALD-Based High Voltage Divider and Signal Circuit for MCP-based Photodetectors}Nucl. Instr. Meth. Phys. Res. A; Vol. 780, Pages 107-113 (April 2014)
PSEC-4 Waveform Sampling Chip E. Oberla, J.-F. Genat, H. Grabas, H. Frisch, K. Nishimura, and G Varner
A 15 GSa/s, 1.5 GHz Bandwidth Waveform Digitizing ASIC;
Nucl. Instr. Meth. A735, Jan., 2014, http://dx.doi.org/10.1016/j.nima.2013.09.042; http://arxiv.org/abs/1309.4397
Our Published PSEC Papers-p1

## Slide 32: Microstrip Anode RF Performance H. Grabas, R. Obaid, E. Oberla, H. Frisch J.-F. Genat, R. Northrop, F. Tang, D. McGinnis, B. Adams, and M. Wetstein; RF Strip-line Anodes for Psec Large-area MCP-based Photodetectors, Nucl. Instr. Meth. A71, pp124-131, May 2013
Our Published PSEC Papers –p2
MCP Testing and Pulse Performance : B. Adams, M. Chollet, A. Elagin, A. Vostrikov, M. Wetstein, R. Obaid, and P. Webster
A Test-facility for Large-Area Microchannel Plate Detector Assemblies using a Pulse Sub-picosecond Laser;
Review of Scientific Instruments 84, 061301 (Oct. 2013)
The OTPC E. Oberla et al. Performance of a Prototype Optical Time Projection Chamber; to be submitted to Nucl. Instr. Meth. summer 2015
In Preparation

## Slide 33: Many Thanks to:
Our Collaborators at ANL-ESD, ANL-XSD, ANL-MSD, UC-Berkeley SSL, Hawai’i, BNL and Cornell (esp. Joe Gregar, Ossy, Gary, Klaus, Bernhard, and Luca)
Staff and management at Incom, Arradiance, InnoSys, and RMD corporations (esp. Michael)
The Fermilab Mcenter Test Beam Crew and LArIAT (esp. JJ)
Others in the field of fast-timing , with special thanks to T. Ohshima and J. Vavra; and waveform sampling, (special thanks here to D. Breton, E. Delagnes, J.F.-Genat, S. Ritt, and G. Varner)
Howard Nicholson and the US DOE Office of HEP; Shawn, John, and the ARL staff
Our EFI staff (!) - Rich Northrop, Mircea Bogdan, Fukun Tang, Mary Heintz, Bob Metz, and Holly Hernandez

## Slide 34: The End

## Slide 35: Backup Slides