## Slide 1: The Development of Large-Area Pico-second Photodetectors
Henry Frisch, Enrico Fermi Institute, Univ. of Chicago
For the LAPPD Collaboration

## Slide 2: Outline
New Types of Detectors Can Change Whole Areas of Science, Medical Imaging, Nuclear Non-proliferation
Technical details of LAPPD: Surface Physics, GigaHz E&M, Glass, Circuit (ASIC) design, Tech Transfer to Industry
Photocathodes- learning SS physics (!)
Opportunities – many PhD theses in many fields- a broad collaborative effort, including industry
Acknowledgements- LAPPD collaborators, Howard Nicholson and the DOE HEP, ANL Management, and the NSF.

## Slide 3: Why has 100 psec been the # for 60 yrs?
Typical path lengths for light and electrons are set by physical dimensions of the light collection and amplifying device.
These are on the order of an inch. One inch is 100 psec. That’s what we measure- no surprise! (LH picture from T. Credo)
Typical Light Source (With Bounces)
Typical PMT’s (With Long Path Lengths)

## Slide 4: Colliders:
Differential TOF: measure the difference in arrival times of photons and charged particles which arrive a few psec later (gives precise local time-dependent calibration
1) Identify the quark content of charged particles;
2) Vertex photons ; 3) Separate vertices; 4) Discovery
Extract all the information in each event (4-vectors) – only spins remain…
Light source is Cherenkov light in the window or radiator.
Will come back to this at the end…

## Slide 5
Need, e.g.- Higgs to gamma-gamma at the LHC - tie the photons to the correct vertex, and more precisely reconstruct the mass of the pair
Major problem coming up at LHC- vertexing at high luminosity (e.g. Joe Incandela’s UC seminar on CMS)
Time (ns)
Vertex position along beam line (cm)
3 different interactions in one beam crossing
Multi-vertex event at CDF (Tevatron)

## Slide 6: Neutrino Physics
Approach: measure the arrival times and positions of photons and reconstruct tracks in water
Benefit: Factor of 5 less volume needed, cost.
Need: lower the cost and extend the reach of large neutrino detectors
Competition- large PMT’s, Liquid Argon
H. Nicholson

## Slide 7: A Photon Time-Projection Chamber
Work of Matt Wetstein (Argonne,&Chicago) in his spare time (sic)

## Slide 8: Daniel Boone*
Proposal (LDRD) to build a little proto-type to test photon-TPC ideas and as a simulation testbed
`Book-on-end’ geometry- long, higher than wide
Close to 100% coverage so bigger Fid/Tot volume
Dx, Dy << 1 cm
Dt < 100 psec
Magnetic field in volume
Idea: to reconstruct vertices, tracks, events as in a TPC (or, as in LiA).
n
2 m
2 m
1 m
caps
Daniel
Also ANNIE- Bob Svoboda
* Think MiniBoone, etc

## Slide 9
(T1, X1, Y1 )
(T2, X2, Y2 )
Vertex (e.g. p0->gg)
Tv, Xv, Yv, Zv
Photon 1
Photon 2
Detector Plane
One can reconstruct the vertex from the times and positions- 3D reconstruction
(t1-tv)c
(t2-tv)c
Rare Kaon Decays- backgd rejection by reconstructing p0 vertex space point:
E.g. for KOTO (Yau Wah, JPARC)-beat down combinatoric p0 bkgds

## Slide 10: Sampling Calorimetry in PET (1B$ Mkt)
Depth in crystal by time-difference
Heejong Kim
Heejong Kim
Can we solve the depth-of-interaction problem and also use cheaper faster radiators?
Alternating radiator and cheap 30-50 psec planar mcp-pmt’s on each side
Depth in crystal by energy- asymmetry
Simulations by Heejong Kim (Chicago)

## Slide 11: Cherenkov-sensitive Sampling Quasi- Digital EM/Had-separating Calorimeters
A picture of an em shower in a cloud-chamber with ½” Pb plates (Rossi, p215- from CY Chao)
A `cartoon’ of a fixed target geometry such as for JPARC’s KL-> pizero nunubar (at UC, Yao Wah) or LHCb

## Slide 12: How Does it Work?
Requires large-area, gain > 107, low noise, low-power, long life, 
(t)<10 psec, (x) < 1mm, and low large-area system cost
Realized that an MCP-PMT has all these but large-area, low-cost:
(since intrinsic time and space scales are set by the pore sizes- 2-20µ)
window
Photocathode on inside of window
Pair of micro-channel plates
RF strip-line anode
Incoming charged particle
Photo-electron
from cathode
Radiated Cherenkov photon
Output pulse of 107 electrons

## Slide 13: Simplifying MCP Construction
Chemically produced and treated Pb-glass does 3-functions:
Provide pores
Resistive layer supplies electric field in the pore
Pb-oxide layer provides secondary electron emission
Conventional Pb-glass MCP
OLD
Incom Glass Substrate
NEW
Separate the three functions:
Hard glass substrate provides pores;
Tuned Resistive Layer (ALD) provides current for electric field (possible NTC?);
Specific Emitting layer provides SEE

## Slide 14: Micro-Channel Plate Development
Simulation of electric field in 1 or several pores- with endspoiling; (attempted) comparison with data
Incom 8”-sq high-quality MCP plate with > 65% OAR

## Slide 15: Incom Micropore Substrate
.075”
~150 20m pores
INCOM glass substrate
Incom.inc, Charlton Mass
80 million 20-micron pores in an 8”-sq plate
65% open-area ratio; 1.2mm thick (L/D=60)

## Slide 16: New MCP Structure (not to scale)
16
resistive coating (ALD)
emissive coating (ALD)
conductive coating (thermal evaporation or sputtering)
pore
1 KV
Jeff Elam
Notes: Very schematic – not correct open area ratio
Might need to do Au before Al2O3 for better contact
Add HV leads
16

## Slide 17: Atomic Layer Deposition (ALD) Thin Film Coating Technology
Atomic level thickness control
Deposit nearly any material
Precise coatings on 3-D objects (JE)
Jeff Elam pictures
Lots of possible materials => much room for higher performance
Notes: 17
For the technologies that I’ll be describing today, ALD has attributes that uniquely suit it

## Slide 18
Slade Jokela (ANL)

## Slide 19
ALD-Coated Incom 8” by 8” Microchannel Plate
80,000,000 pores
Anil Mane and Jeff Elam (ANL)
A commercial 2”-square plate is more than $1000 and isn’t as good in many ways

## Slide 20: ALD &Integration tests at ANL
Anil Mani and Bob Wagner
20
Razib Obaid and Matt Wetstein
Bernhard Adams, Andrei Elagin, Razib Obaid, Eric Oberla, Matt Wetstein
Using <100 Femtosec laser, lots of vacuum (sic)
ALD-coated MCP plate (Anil)

## Slide 21: Microchannel Plates-4b
Noise (bkgd rate).
<=0.1 counts/cm2/sec; factors of few > cosmics (!)
Ossy Siegmund, Jason McPhate, Sharon Jelinsky, SSL/UCB
Performance:

## Slide 22: Microchannel Plates-4d
Performance: burn-in (aka `scrub’)
Measurements by
Ossy Siegmund,
Jason McPhate,
Sharon Jelinsky, SSL/UCB
Typical MCP behavior- long scrub-times
Measured ANL ALD-MCP behavior
(ALD by Anil Mane, Jeff Elam, ANL)
(Big deal commercially?)

## Slide 23: Signal- want large for S/N
We see gains > 107 in a chevron-pair
Ossy Siegmund, Jason McPhate, Sharon Jelinsky, SSL/UCB
ALD by Anil Mane and Jeff Elam, ANL

## Slide 24: The Half-Meter-Squared SuperModule
A `tile’ is a sealed vacuum-tube with cathode, 2 MCP’s, RF-strip anode, and internal voltage divider
HV string is made with ALD
A SuperModule holds 12 tiles in 3 tile-rows. 15 waveform sampling ASICS on each end of the tray digitize 90 strips. 2 layers of local processing (Altera) measure extract charge, time, position, goodness-of-fit

## Slide 25: Demonstrated Position Sensitivity
Razib’s scanning stage
4-tile `tile-row’
of Supermodule
Time difference of 2 ends vs laser position

## Slide 26: Demonstration of the Internal ALD HV Divider in the Demountable Tile
Demountable at APS
Scanning the laser: t vs x
Average pulse shape vs HV
IV Curve (expected 32 Megs)

## Slide 27: Developing and Testing the Electronics, Anodes, and DAQ
Eric Oberla (grad student) and Craig Harabedian (engineer) working on the Tray layout and cabling

## Slide 28: Anode Testing for ABW, Crosstalk,..
Network Analyzer Tile Anode
Herve’ Grabas, Razib Obaid, Dave McGinnis

## Slide 29: Anode Testing for ABW, Crosstalk,..
Razib Obaid
Crosstalk
ABW

## Slide 30
PSEC-4 ASIC
6-channel “oscilloscope on a chip” (1.6 GHz,10-15 GS/s)
Evaluation board uses USB 2.0 interface + PC data acquisition software
LAPPD Collaboration
Eric Oberla, ANT11

## Slide 31: 6-channel `Scope-on-a-chip’
20 GS/scope
4-channels (142K$)
17 GS/PSEC-4 chip
6-channels ($130 ?!)
Real digitized traces from anode
Designed by Eric Oberla (UC grad student)
working in EDG
with EDG tools and engineers
(H. Grabas, J.F. Genat)

## Slide 32
PSEC-4 Performance
Digitized Waveforms
Input: 800MHz, 300 mVpp sine
Sampling rate : 10 GSa/s
Sampling rate : 13.3 GSa/s
Only simple pedestal correction to data
As the sampling rate-to-input frequency ratio decreases, the need for time-base calibration becomes more apparent (depending on necessary timing resolution)
Eric Oberla, ANT11

## Slide 33: Photocathodes
LAPPD goal- 20-25% QE, 8”-square- conv. alkali
2 parallel efforts: SSL (knows how), and ANL (learning)
ANL
Optical stand
First cathodes made at ANL
Burle commercial
equipment

## Slide 34: Status of PhotoCathodes
Have made >20% 8”PC at SSL; 25% small PC’s at ANL, 18% 4” (larger underway)
SSL 8” SbNaK cathode
4” cathode: Chalice in Burle oven
QE of SSL 8” SbNaK cathode
QE of ANL small SbKCs cathodes
ANL
ANL

## Slide 35: PhotoCathode Research
Ongoing collaboration with BNL, UCB, UC, ANL for `Theory-Based Photocathodes
Xray diffraction while growing
Razib, Carlos, and Junqi put a PMT into
an APS Xray beam (you should ask them any questions…)

## Slide 36: Conclusions

## Slide 37: 8”-MCP Pair and Strip Anode Work
Laser mirrors and 8” anode for 8” MCP tests
Pulses from one strip of 8” anode with 8” MCP pair
Matt Wetstein, Bernhard Adams, Andrey Elagin, Razib Obaid, Sasha Vostrikov, Bob Wagner

## Slide 38: Demonstrated Position Sensitivity
Razib’s scanning stage
4-tile `tile-row’
of Supermodule
Time difference of 2 ends vs laser position

## Slide 39: Timing res agrees with MC
Time resolution on 2 ends of 8”-anode strip vs (S/N)-1 in psec (pair of 8” MCP’s)
< 6 psec
M. Wetstein, B. Adams, A. Elagin, R. Obaid, A. Vostrikov, …
Laser spot
size

## Slide 40: Going Another Order-of-Magnitude
100 Femtosec (!)
Stefan Ritt slide, doctored
Subject of a 2013 SBIR with Innosys, SLC
(agrees with JF MC)
1.0
0.7
17
1.6
17
Achieved by LAPPD
For 100 fsec
Dt: g e p K p
(ps) 0 10-6 0.13 1.6 6.25
Differential TOF:
1.5m path

## Slide 41: What’s the limit? (2009 cartoon)
Front Window and Radiator
Photocathode
Pump Gap
High Emissivity Material
Low Emissivity Material
`Normal’ MCP pore material
Gold Anode
50 Ohm Transmission Line
Rogers PC Card
Capacitive Pickup to Sampling Readout
N.B.- this is a `cartoon’- working on workable designs-join us…
Funnel pore with reflection cathode, dynode rings, ceramic anode,…

## Slide 42: Comparison with existing detectors
K. Arisaka; UCLA
Psec
Cm2

## Slide 43: More Information on LAPPD:
Main Page: http://psec.uchicago.edu (has the links to the Library and Blogs)
Library: Workshops, Godparent Reviews, Image Library, Document Library, Links to MCP, Photocathode, Materials Literature, etc.;
Blog: Our log-book- open to all (say yes to certificate Cerberus, etc.)- can keep track of us (at least several companies do);

## Slide 44: The End